## Slide 1: Unit III Multiprocessors and Thread-Level Parallelism
By
N.R.Rejin Paul
Lecturer/VIT/CSE
CS2354 Advanced Computer Architecture

## Slide 2: Chapter 6. Multiprocessors and Thread-Level Parallelism
<number>
6.1 Introduction
6.2 Characteristics of Application Domains
6.3 Symmetric Shared-Memory Architectures
6.4 Performance of Symmetric Shared-Memory Multiprocessors
6.5 Distributed Shared-Memory Architectures
6.6 Performance of Distributed Shared-Memory Multiprocessors
6.7 Synchronization
6.8 Models of Memory Consistency: An Introduction
6.9 Multithreading: Exploiting Thread-Level Parallelism within a Processor

## Slide 3: Taxonomy of Parallel Architectures
<number>
Flynn Categories
SISD (Single Instruction Single Data)
  Uniprocessors
MISD (Multiple Instruction Single Data)
  ???; multiple processors on a single data stream
SIMD (Single Instruction Multiple Data)
  same instruction executed by multiple processors using different data streams
    Each processor has its data memory (hence multiple data)
    There’s a single instruction memory and control processor
  Simple programming model, Low overhead, Flexibility
  (Phrase reused by Intel marketing for media instructions ~ vector)
  Examples: vector architectures, Illiac-IV, CM-2
MIMD (Multiple Instruction Multiple Data)
  Each processor fetches its own instructions and operates on its own data
  MIMD current winner: Concentrate on major design emphasis <= 128 processors
    Use off-the-shelf microprocessors: cost-performance advantages
    Flexible: high performance for one application, running many tasks simultaneously
  Examples: Sun Enterprise 5000, Cray T3D, SGI Origin

## Slide 4: MIMD Class 1: Centralized shared-memory multiprocessor
<number>
share a single centralized memory, interconnect processors and memory by a bus
also known as “uniform memory access” time taken to access from all processor to memory is same (UMA) or “symmetric (shared-memory) multiprocessor” (SMP)
  A symmetric relationship to all processors
  A uniform memory access time from any processor
scalability problem: less attractive for large-scale processors

## Slide 5: MIMD Class 2: Distributed-memory multiprocessor
<number>
memory modules associated with CPUs
Advantages:
  cost-effective way to scale memory bandwidth
  lower memory latency for local memory access
Drawbacks
  longer communication latency for communicating data between processors
  software model more complex

## Slide 6: 6.3 Symmetric Shared-Memory Architectures
<number>
Each processor have same relationship to single memory
usually supports caching both private data and shared data
Caching in shared-memory machines
private data: data used by a single processor
  When a private item is cached, its location is migrated to the cache
  Since no other processor uses the data, the program behavior is identical to that in a uniprocessor
shared data: data used by multiple processor
  When shared data are cached, the shared value may be replicated in multiple caches
  advantages: reduce access latency and fulfill bandwidth requirements, due to difference in communication for load store and strategy to write from caches values form diff. caches may not be consistent
  induce a new problem: cache coherence
Coherence cache provides:
migration: a data item can be moved to a local cache and used there in a transparent fashion
replication for shared data that are being simultaneously read
both are critical to performance in accessing shared data

## Slide 7: Multiprocessor Cache Coherence Problem
<number>
Informally:
  “memory system is coherent if Any read must return the most recent write”
  Coherent – defines what value can be returned by a read
  Consistency – that determines when a return value will be returned by a read
  Too strict and too difficult to implement
Better:
  Write propagation : value return must visible to other caches “Any write must eventually be seen by a read”
  All writes are seen in proper order by all caches(“serialization”)
Two rules to ensure this:
  “If P writes x and then P1 reads it, P’s write will be seen by P1 if the read and write are sufficiently far apart”
  Writes to a single location are serialized: seen in one order
    Latest write will be seen
    Otherwise could see writes in illogical order (could see older value after a newer value)
Notes: <number>

## Slide 8: Example Cache Coherence Problem
<number>
  Processors see different values for u after event 3
I/O devices
Memory
P
1
$
$
$
P
2
P
3
5
u
= ?
4
u
= ?
u
:5
1
u
:5
2
u
:5
3
u
= 7

## Slide 9: Defining Coherent Memory System
<number>
Preserve Program Order: A read by processor P to location X that follows a write by P to X, with no writes of X by another processor occurring between the write and the read by P, always returns the value written by P
Coherent view of memory: Read by a processor to location X that follows a write by another processor to X returns the written value if the read and write are sufficiently separated in time and no other writes to X occur between the two accesses
Write serialization: 2 writes to same location by any 2 processors are seen in the same order by all processors
  For example, if the values 1 and then 2 are written to a location X by P1 and P2, processors can never read the value of the location X as 2 and then later read it as 1

## Slide 10: Basic Schemes for Enforcing Coherence
<number>
Program on multiple processors will normally have copies of the same data in several caches
Rather than trying to avoid sharing in SW, SMPs use a HW protocol to maintain coherent caches
  Migration and Replication key to performance of shared data
Migration - data can be moved to a local cache and used there in a transparent fashion
  Reduces both latency to access shared data that is allocated remotely and bandwidth demand on the shared memory
Replication – for shared data being simultaneously read, since caches make a copy of data in local cache
  Reduces both latency of access and contention for reading shared data

## Slide 11: 2 Classes of Cache Coherence Protocols
<number>
Snooping — Every cache with a copy of data also has a copy of sharing status of block, but no centralized state is kept
  All caches are accessible via some broadcast medium (a bus or switch)
  All cache controllers monitor or snoop on the medium to determine whether or not they have a copy of a block that is requested on a bus or switch access
Directory based — Sharing status of a block of physical memory is kept in just one location, the directory

## Slide 12: Snoopy Cache-Coherence Protocols
<number>
Cache Controller “snoops” all transactions on the shared medium (bus or switch)
  relevant transaction if for a block it contains
  take action to ensure coherence
    invalidate, update, or supply value
  depends on state of the block and the protocol
Either get exclusive access before write via write invalidate or update all copies on write
State
Address (tag)
Data

## Slide 13: Example: Write-thru Invalidate
<number>
Must invalidate before step 3
Write update uses more broadcast medium BW  all recent MPUs use write invalidate
I/O devices
Memory
P
1
$
$
$
P
2
P
3
5
u
= ?
4
u
= ?
u
:5
1
u
:5
2
u
:5
3
u
= 7
u = 7

## Slide 14: Two Classes of Cache Coherence Protocols
<number>
Snooping Solution (Snoopy Bus)
  Send all requests for data to all processors
  Processors snoop to see if they have a copy and respond accordingly
  Requires broadcast, since caching information is at processors
  Works well with bus (natural broadcast medium)
  Dominates for small scale machines (most of the market)
Directory-Based Schemes (Section 6.5)
  Directory keeps track of what is being shared in a centralized place
  Distributed memory => distributed directory for scalability (avoids bottlenecks)
  Send point-to-point requests to processors via network
  Scales better than Snooping
  Actually existed BEFORE Snooping-based schemes

## Slide 15: Basic Snoopy Protocols
<number>
Write strategies
  Write-through: memory is always up-to-date
  Write-back: snoop in caches to find most recent copy
  There are two ways to maintain coherence requirements using snooping protocols
Write Invalidate Protocol
  Multiple readers, single writer
  Write to shared data: an invalidate is sent to all caches which snoop and invalidate any copies
    Read miss: further read will miss in the cache and fetch a new copy of the data
Write Broadcast/Update Protocol
  Write to shared data: broadcast on bus, processors snoop, and update any copies
  Read miss: memory/cache is always up-to-date
Write serialization: bus serializes requests!
  Bus is single point of arbitration

## Slide 16: Examples of Basic Snooping Protocols
<number>
Assume neither cache initially holds X and the value of X in memory is 0
Write Invalidate
Write Update

## Slide 17: An Example Snoopy Protocol
<number>
Invalidation protocol, write-back cache
Each cache block is in one state (track these):
  Shared : block can be read
  OR Exclusive : cache has only copy, its writeable, and dirty
  OR Invalid : block contains no data
  an extra state bit (shared/exclusive) associated with a valid bit and a dirty bit for each block
Each block of memory is in one state:
  Clean in all caches and up-to-date in memory (Shared)
  OR Dirty in exactly one cache (Exclusive)
  OR Not in any caches
Each processor snoops every address placed on the bus
  If a processor finds that is has a dirty copy of the requested cache block, it provides that cache block in response to the read request

## Slide 18: Cache Coherence Mechanism of the Example
<number>
Placing a write miss on the bus when a write hits in the shared state ensures an exclusive copy (data not transferred)

## Slide 19: Figure 6.11 State Transitions for Each Cache Block
<number>
CPU may read/write hit/miss to the block
May place write/read miss on bus
May receive read/write miss from bus
Requests from CPU
Requests from bus

## Slide 20: Cache Coherence State Diagram
<number>
Figure 6.10 and Figure 6.12 (CPU in black and bus in gray from Figure 6.11)

## Slide 21: 6.5 Distributed Shared-Memory Architectures
<number>
Distributed shared-memory architectures
Separate memory per processor
  Local or remote access via memory controller
  The physical address space is statically distributed
Coherence Problems
Simple approach: uncacheable
  shared data are marked as uncacheable and only private data are kept in caches
  very long latency to access memory for shared data
Alternative: directory for memory blocks
  The directory per memory tracks state of every block in every cache
    which caches have a copies of the memory block, dirty vs. clean, ...
  Two additional complications
    The interconnect cannot be used as a single point of arbitration like the bus
    Because the interconnect is message oriented, many messages must have explicit responses
Notes: <number>

## Slide 22: Distributed Directory Multiprocessor
<number>
To prevent directory becoming the bottleneck, we distribute directory entries with memory, each keeping track of which processors have copies of their memory blocks
Notes: <number>

## Slide 23: Directory Protocols
<number>
Similar to Snoopy Protocol: Three states
  Shared: 1 or more processors have the block cached, and the value in memory is up-to-date (as well as in all the caches)
  Uncached: no processor has a copy of the cache block (not valid in any cache)
  Exclusive: Exactly one processor has a copy of the cache block, and it has written the block, so the memory copy is out of date
    The processor is called the owner of the block
In addition to tracking the state of each cache block, we must track the processors that have copies of the block when it is shared (usually a bit vector for each memory block: 1 if processor has copy)
Keep it simple(r):
  Writes to non-exclusive data => write miss
  Processor blocks until access completes
  Assume messages received and acted upon in order sent
Notes: <number>

## Slide 24: Messages for Directory Protocols
<number>
local node: the node where a request originates
home node: the node where the memory location and directory entry of an address reside
remote node: the node that has a copy of a cache block (exclusive or shared)

## Slide 25: State Transition Diagram for Individual Cache Block
<number>
Comparing to snooping protocols:
  identical states
  stimulus is almost identical
  write a shared cache block is treated as a write miss (without fetch the block)
  cache block must be in exclusive state when it is written
  any shared block must be up to date in memory
write miss: data fetch and selective invalidate operations sent by the directory controller (broadcast in snooping protocols)

## Slide 26: State Transition Diagram for the Directory
<number>
Figure 6.29 Transition diagram for cache block
Three requests: read miss, write miss and data write back

## Slide 27: Directory Operations: Requests and Actions
<number>
Message sent to directory causes two actions:
  Update the directory
  More messages to satisfy request
Block is in Uncached state: the copy in memory is the current value; only possible requests for that block are:
  Read miss: requesting processor sent data from memory &requestor made only sharing node; state of block made Shared.
  Write miss: requesting processor is sent the value & becomes the Sharing node. The block is made Exclusive to indicate that the only valid copy is cached. Sharers indicates the identity of the owner.
Block is Shared => the memory value is up-to-date:
  Read miss: requesting processor is sent back the data from memory & requesting processor is added to the sharing set.
  Write miss: requesting processor is sent the value. All processors in the set Sharers are sent invalidate messages, & Sharers is set to identity of requesting processor. The state of the block is made Exclusive.
Notes: <number>

## Slide 28: Directory Operations: Requests and Actions (cont.)
<number>
Block is Exclusive: current value of the block is held in the cache of the processor identified by the set Sharers (the owner) => three possible directory requests:
  Read miss: owner processor sent data fetch message, causing state of block in owner’s cache to transition to Shared and causes owner to send data to directory, where it is written to memory & sent back to requesting processor. Identity of requesting processor is added to set Sharers, which still contains the identity of the processor that was the owner (since it still has a readable copy). State is shared.
  Data write-back: owner processor is replacing the block and hence must write it back, making memory copy up-to-date (the home directory essentially becomes the owner), the block is now Uncached, and the Sharer set is empty.
  Write miss: block has a new owner. A message is sent to old owner causing the cache to send the value of the block to the directory from which it is sent to the requesting processor, which becomes the new owner. Sharers is set to identity of new owner, and state of block is made Exclusive.
Notes: <number>

## Slide 29: Summary
<number>
Chapter 6. Multiprocessors and Thread-Level Parallelism
6.1 Introduction
6.2 Characteristics of Application Domains
6.3 Symmetric Shared-Memory Architectures
6.4 Performance of Symmetric Shared-Memory Multiprocessors
6.5 Distributed Shared-Memory Architectures
6.6 Performance of Distributed Shared-Memory Multiprocessors
6.7 Synchronization
6.8 Models of Memory Consistency: An Introduction
6.9 Multithreading: Exploiting Thread-Level Parallelism within a Processor